## Slide 1: Module 1
Introduction to the course

## Slide 2: General Information
Course: Computer Organization (IT 209)
Instructor: Amit Bhatt
TAs: Total 10
3-0-2-4
Text books:
  ARM assembly language by William Hohl
  Computer Organization and Design by Patterson and Hennessey
  ARM System Developer’s Guide By Andrew N. Sloss, Dominic Symes, Chris Wright, Published by Elsevier (Optional)

## Slide 3: Grading Policy
30% Midterm 1 -> Most probably lab exam
30% Midterm 2
40% Final exam
Negative marks for not submitting your homework assignments
Important: Attendance will be taken on some days. You need to attain 80% attendance in those days when attendance was taken. If you miss the quiz, then NO MAKEUP EXAM will be administered under any excuse. You will get zero marks

## Slide 7: IT 209 Course Outline Computer Organization

## Slide 8: Course Outline
Module 1:
  Course outline, Grading policy, Goals and importance of the course
Module 2:
  Explanation of the components of the processors
    History of computers
    How can a processor understand your program and concept of Instructions
    Registers
    Program counter
    Memory / stored program concept
    ALU
    Pipelines

## Slide 9
Module 3: (Read AAL Ch 4, 5, 6,7)
  Study of ARM ISA version 4T
    Load/Store instructions
    Arithmetical instructions
    Logical instructions
    Control instructions
Module 4: (Read AAL Ch 8, 10 and 14)
  Loops and Branches
  Subroutines and Stacks
    ARM APCS
    Passing parameters to subroutine
  Mixing C and Assembly Language

## Slide 10
Module 5: (Read AAL Ch 11)
  Exception Handling
Module 6:
  Revision
Module 7: (Read COD Ch 4.1, 4.2, 4.3, 4.4)
  Logic design convention
  Building a datapath
Module 8: (Read COD Ch 4.5)
  Over view of Pipelining and Hazards
Module 9: (Read COD Ch 4.6)
  Pipelined Datapath and control

## Slide 11
Module 10:
  Data Hazard (stalling vs forwarding)
Module 11:
  Control Hazard
    Branch Prediction; static and dynamic
    Branch delay slot
Module 12:
  Exceptions in a pipelined processor
  Concept of Instruction level parallelism (ILP)
  Loop level parallelism (LLP)
  Superscalar processor
  VLIW processor

## Slide 12
Module 13:
  Memory hierarchy
Module 14 Revision
Up to five lectures will be used for in – class tutorial and quiz

## Slide 13: IT – 209, Computer Organization…
What is Computer Organization?
  It refers to the level of abstraction above the digital logic level, but below the operating system level
  Major components are Processor, I/O system, Memory, Data Path and Control
Do I need IT-209 course? How will it help me in
  Getting a job?
  Higher Academic studies?

## Slide 14: Where are the Processors?
How many Processors do you have in your house?

## Slide 15
Mobile Phone (average 2.6 processors)
Tablet (more than 3)
Car (average 10 – 35)
iPod
Set top box for TV
microwave oven, washer, dryer, dishwasher, coffee maker, refrigerator, television, video-game console, stereo receiver, CD player, DVD player, remote control for the TV…

## Slide 16: Number of Processor Sold World-wide?
Guess?

## Slide 17: Historical view
Introduction of a new category
  High Performance Computing (HPC)
  Desktop/Laptop/Server Intel
  Smartphones (MID)
  Embedded System ARM

## Slide 18: Battle of Architecture: Intel vs ARM vs RISC V
How many types of Architectures are there?
When we say Architecture, we mean Instruction Set Architecture (ISA)
Intel architecture is generally known as x86 architecture
Some architectures are almost dead – MIPS architecture

## Slide 19: About Intel (INTC)
Founded on July 18th 1968 named as Integrated Electronics Corporation
Market Capitalization: $231.65B (as on June 2018)
P/E ratio 17.61
Employee Count ~ 107,400
First Chip (4004) developed in 1971
Notes: Founders: Gordon Moore, Robert Noyce (co-inventer of IC) and Arthur Rock (investor). Before naming the company as INTEL, they called it Moore-Noyce (a big no no since it is a homophone for More Noise). For a year it was known as NM electronics. Intel was a trademark owned by the hotel chain Intelco, they had to buy the rights.
Till 1981, Intel’s major business was DRAM and SRAM. In 1983, CEO Decided to focus on micro-processor business
Unprecedented growth since 1990 due to success of Intel inside campaign.
Intel has adopted tick-tock model (annual alternation of microarchitecture innovation and process innovation)
In 2006, Intel produced p6 and NetBurst products at 65nm followed a year later by Core architecture
Intel intorduced Pneryn microarchitecture and underwent a shrink from 65 to 45 (in 2008)
Next year got Successor processor Nehalem followed by another shrink to 32nm.

## Slide 20: RISC V
New kid on the block
Open software – no license fees or royalty…
Founded by Krste Asanovich in Berkeley
Commercial wing of RISC V foundation is known as SiFive
Purchased OpenSilicon in India

## Slide 21: ARM (ARMH)
Started life as Acorn Computer in 1985
ARM hived off as a separate company in 1991
Total Market Capitalization 19.0B
P/E ratio 8301.47 (till acquisition by softbank)
Manpower ~ 2600
Originally a British company,
Now acquired by the Softbank
of Japan

## Slide 22: ARM Ltd
Founded in November 1990
  Spun out of Acorn Computers
Designs the ARM range of RISC processor cores
Licenses ARM core designs to semiconductor partners who fabricate and sell to their customers.
  ARM does not fabricate silicon itself
Also develop technologies to assist with the design-in of the ARM architecture
  Software tools, boards, debug hardware, application software, bus architectures, peripherals etc
Notes: The ARM processor core originates within a British computer company called Acorn. In the mid-1980s they were looking for replacement for the 6502 processor used in their BBC computer range, which were widely used in UK schools. None of the 16-bit architectures becoming available at that time met their requirements, so they designed their own 32-bit processor.
Other companies became interested in this processor, including Apple who were looking for a processor for their PDA project (which became the Newton). After much discussion this led to Acorn’s processor design team splitting off from Acorn at the end of 1990 to become Advanced RISC Machines Ltd, now just ARM Ltd.
Thus ARM Ltd now designs the ARM family of RISC processor cores, together with a range of other supporting technologies.
One important point about ARM is that it does not fabricate silicon itself, but instead just produces the design - we are an Intellectual Property (or IP) company. Instead silicon is produced by companies who license the ARM processor design.

## Slide 23: ARM’s Activities
memory
SoC
Processors
System Level IP:
Data Engines
Fabric
3D Graphics
Physical IP
Software IP
Development Tools
Connected Community
Notes: The slide helps explain where ARM products play. A generic Digital product; ARM supplies system level IP into the SoC along with Physical IP to ensure its manufacturable;
Software IP into the system; Development tools to help design and build the system architecture and software.
Finally, we work with an extensive 3rd party community to make the whole device creation possible.
Remember this helps frame what we do not cover also, e.g. industrial design of the device.

## Slide 24
ARM Eco-System

## Slide 25: ARM Processor Applications

## Slide 26: ARM…
100 billion chips shipped between 1991 – 2018
50 billion chips shipped between 2013-2017
Next 100 billion by 2022!!

## Slide 27: Some important qualities of ARM processors
ARM processors follows RISC architecture philosophy (but it is not a pure RISC processor)
ARM processors are generally used in mobile devices hence they are specifically designed to consume low power
ARM Embedded processors (ARM 7,9, Cortex M0+, M3) are generally used in applications which have limited memory due to cost or size consideration, hence high code density is one of the major requirement
ARM processors are designed to take up minimum die area because higher the die size, higher the cost

## Slide 28: Reduced Instruction Set Computer Philosophy
RISC is a term coined by Berkeley
It was invented to counter the philosophy used by Intel which was known as Complex Instruction Set Computer (CISC)
Rules of RISC
  Instructions: use a minimum number of simple instructions which can execute in 1 cycle. Complex operations are done by using combination of simple instructions
  Pipelines: Processing of instructions is broken down in to smaller units so as to increase throughput
  RISC machine have a large number of general purpose registers. Any register can either have data or memory address
  Load-Store architecture: data memory can be access only though load and store instruction

## Slide 29: ARM Architecture and Processor
An architecture defines behaviour that is common to many processor designs
This would include
  The instruction set
  Registers
  Exception handling
  Memory model

## Slide 30: What is an Instruction and How it is executed?
Op Code
Destination
Source 1
Source 2
Stored Program Concept

## Slide 31: Difference between Architecture & implementation
ARMv4
x1-4
ARMv5
ARMv6
ARMv7-Cortex
ARM966E-S
SC200
ARM7EJ-S
ARM922T
SC100
ARM920T
ARM7TDMI(S)
ARM1176JZ(F)-S
ARM1156T2(F)-S
ARM1136J(F)-S
ARM1026EJ-S
ARM968E-S
ARM926EJ-S
ARM946E-S
x1-4
Cortex-A9
SC300
Cortex-M1
Cortex-M3
Cortex-R4
Cortex-R4F
Cortex-A8
ARM11 MPCore
Notes: An architecture defines behaviour that is common to many
processor designs.
The ARM architecture defines how an ARM processor must operate. This includes:
• the programmers model
• the instruction set
• system configuration
• exception handling
• the memory model.
A processor is an implementation of an architecture, and can be
integrated into several different designs

## Slide 32: ARM Processor Naming Convention ARM{x}{y}{z}{T}{D}{M}{I}{E}{J}{F} – {S}
x: Family Name
y: Memory Management / Protection Unit
z: Cache
T: Thumb Instruction set
D: JTAG Debug Facility
M: Fast Multiplier
I: In Circuit Emulation (ICE)
E: Extended (Media related instructions), assumes TDMI
J: Jazzel
s: Synthesizable

## Slide 33: Relative Performance*
*Represents attainable speeds in 130, 90 or 65nm processes
Chart: Processor
ARM7TDMI-S | 184
ARM920T | 250
ARM926EJ-S | 470
ARM1026EJ-S | 540
ARM1136J-S | 610
ARM1176JZ-S | 750
Cortex A8 | 1100
Cortex A8
ARM1176JZ-S
ARM926EJ-S
ARM920T
ARM7TDMI
ARM1136J-S
ARM1026EJ-S
0.43
0.36
0.568
0.335
0.235
0.25
0.35
mW/MHz

## Slide 34: Details about ARM Architecture
It is a RISC based Architecture (Really?)
RISC vs CISC debate
Evolution of ARM architecture

## Slide 35: ARM Architectural History
V4T | V5 | V6 | V7
Half word and Signed Half word support | Improved ARM – Thumb interworking | SIMD instructions | Thumb 2
System Mode | CLZ (count leading Zeros instruction) | Multiprocessing | NEON
Thumb Instruction set | Saturated Math | V6 Memory architecture | Trust Zone
 | DSP MAC instructions | Unaligned data support | Profiles: V7A (Applications) NEON V7R (RealTime) Hardware divide V7M (Microcontroler) Hardware divide Thumb-2 only
 | Extensions: Jazelle (V5TEJ) | Extensions: Thumb-2 (V6T2) Trustzone (V6Z) Multicore (V6K) Thumb Only (V6M) | 

## Slide 36: How does a processor function
Remember the Stored Program Concept?
What is an instruction?
Types of Instruction in v4T
Load/Store
Change of Flow
Data Operations
Change of Flow
Miscellaneous
MOV PC, Rm
Bcc
BL
BLX

## Slide 37: ARM pipelining Concept
Instruction Fetch
Shift + ALU
Memory
Access
Reg
Write
Reg
Read
Reg
Decode
FETCH
DECODE
EXECUTE
MEMORY
WRITE
ARM9TDMI
ARM or Thumb Inst Decode
Reg Select
Reg
Read
Shift
ALU
Reg
Write
Thumb®ARM decompress
ARM decode
Instruction Fetch
FETCH
DECODE
EXECUTE
ARM7TDMI
Notes: Pipeline Comparison
The point of this foil is to show that with the ARM7TDMI a lot of work was carried out in the execute stage of the pipeline. Now with ARM9TDMI the execute stage has been split out into three stages to allow greater throughput.
This then means the CPI is about 1.5 compared against 1.9 for ARM7TDMI, and the operating frequency is approximately double for ARM9TDMI over ARM7TDMI on the same process. Therefore, at least double the processing power is available.
It is possible for the pipeline to interlock. Forwarding paths have been provided to minimise this as much as possible, but they can still occur. By using a bit of consideration when writing code they can almost be eliminated.

## Slide 38: Data Sizes and Instruction Sets
The ARM is a 32-bit architecture
When used in relation to the ARM:
  Byte means 8 bits
  Halfword means 16 bits (two bytes)
  Word means 32 bits (four bytes)
Most ARM’s implement two instruction sets
  32-bit ARM Instruction Set
  16-bit Thumb Instruction Set
Jazelle cores can also execute Java bytecode
Notes: The cause of confusion here is the term “word” which will mean 16-bits to people with a 16-bit background.
In the ARM world 16-bits is a “halfword” as the architecture is a 32-bit one, whereas “word” means 32-bits.
Java bytecodes are 8-bit instructions designed to be architecture independent. Jazelle transparently executes most bytecodes in hardware and some in highly optimized ARM code. This is due to a tradeoff between hardware complexity (power consumption & silicon area) and speed.

## Slide 39
ARM Instruction Address
Memory word
Byte 0
Byte 1
Byte 2
Byte 8
Byte 4
Byte 5
Byte 6
Byte 7
Byte 3
Byte 12
Byte 16
Byte 17
Byte 18
Byte 10
Byte 11
Byte 15
Byte 19
Byte 13
Byte 9
Byte 14
0
4
12
8
16
Inst 2
Inst 1
Inst 4
Inst 3
Inst 5
Reg Select
Reg
Read
Shift
ALU
Reg
Write
Thumb®ARM decompress
ARM decode
Instruction Fetch
FETCH
DECODE
EXECUTE
Inst 1
Inst 3
Inst 2

## Slide 40: Concept of a Program Counter (PC)
Reg Select
Reg
Read
Shift
ALU
Reg
Write
Thumb®ARM decompress
ARM decode
Instruction Fetch
FETCH
DECODE
EXECUTE
Program counter is a special register which contains
the address of the instruction being fetched
PC
PC - 8
PC - 4
ARM Instruction
PC
PC - 2
PC - 4
Thumb Instruction
Notes: Pipeline Comparison
The point of this foil is to show that with the ARM7TDMI a lot of work was carried out in the execute stage of the pipeline. Now with ARM9TDMI the execute stage has been split out into three stages to allow greater throughput.
This then means the CPI is about 1.5 compared against 1.9 for ARM7TDMI, and the operating frequency is approximately double for ARM9TDMI over ARM7TDMI on the same process. Therefore, at least double the processing power is available.
It is possible for the pipeline to interlock. Forwarding paths have been provided to minimise this as much as possible, but they can still occur. By using a bit of consideration when writing code they can almost be eliminated.

## Slide 41: How ARM 7TDMI works
Fetch
Decode
Execute (ALU)
+ Memory Access
+ Write Back to Reg
Registers
Instruction + Data
Memory (Von Neumann arch)
ADD R1, R2, R3
Program Counter

## Slide 42: The ARM7TDMI Core details
Multiplier
Instruction
Decoder
Address
Incrementer
nRESET
nMREQ
SEQ
ABORT
nIRQ
nFIQ
nRW
MAS[1:0]
LOCK
nCPI
CPA
CPB
nWAIT
MCLK
nOPC
BIGEND
ISYNC
nTRANS
nM[4:0]
D[31:0]
Barrel
Shifter
32 Bit ALU
DBE
Write Data Register
Read Data Register
Address Register
Register Bank
A[31:0]
ABE
and
Control Logic
PC Update
Decode Stage
Instruction Decompression
Incrementer
P
C
A
B
u
s
B
B
u
s
A
L
U
B
u
s
Notes: The ARM Core architecture
The ARM7 core is Von Neumann architecture i.e. instructions and data come in on one bus.
The core uses a LOAD and STORE architecture. i.e. all operations are on the registers. Data is loaded, executed upon and then stored back to memory as required. Block transfer: up to 16 register at once
The main feature of the ARM core is the data path. The data path is:-
Register Bank -> Barrel Shifter (on B bus) -> ALU -> Register Bank
Operations through the data path take one cycle. Consider a basic ADD instruction. ADD r0, r1, r2. The r1 and r2 are read out of the register bank on the A and B buses. The result is calculated in the ALU and written back to r0 via the ALU Bus. ( important: 2 read ports A and B! )
Consider an ADD instruction with a shift. ADD r0, r1, r2, LSL#2 The r1 and r2 are read out of the register bank on the A and B buses. R2 is shifted left by 2 in the barrel shifter, The result is calculated in the ALU as before, and written back to r0 via the ALU Bus.
The basic data path is completed in one cycle ( normally, if no delay due to multiply etc. ). In this cycle the following occurs:-
1) Read 2 operands from the register bank, one via the barrel shifter (to be shifted if required).
2) Implement a logical or arithmetic operation in the ALU.
3) Write back the result to register bank at the end of the cycle.
Can do shifts by a constant in the same cycle in ARM state, but not in Thumb state (where separate instructions are required to use the shifter). Limitation of reduced instruction space.
Instruction pipeline is three stage fetch -> decode -> execute.
Address Incrementer allows for burst mode addressing.
Booth multiplier has early termination if the rest of the operand is 0 or 1. The advantage is that it is small.
Notice the Thumb decompression stage on the instruction pipeline input. This uses a spare half clock cycle on the decode stage of the pipeline, and hence does not restrict the maximum clock speed over non-thumb ARM7’s.
For load operations, sign extension and/or rotation is done in the ALU. (ARM9 is different…see slide 21)

## Slide 43: ARM and Thumb Performance
Memory width (zero wait state)
Chart: 
| 32-bit | 16-bit | 16-bit with 32-bit stack
ARM | 30000 | 16000 | 17500
Thumb | 26000 | 22000 | 24500
Dhrystone 2.1/sec
@ 20MHz
Notes: Intention
To show a comparison of memory usage between ARM and thumb instructions when running from different size memory width.
In 16-bit memory, Thumb code is better. Even though there are more instructions, each instruction only take a single cycle to fetch whereas each ARM instruction now takes two cycles to fetch.
However you can see in the 16-bit example that the performance from Thumb has gone down -despite still taking a single cycle to fetch each instruction. This is because of data accesses, and in particular stack accesses. Even in Thumb, each access to the stack will be a 32-bit quantity (as register contents are transferred - and this lowers performance on a full 16-bit memory architecture.
One way around this is to provide a limited amount of 32-bit memory to place you stack in - which can give a useful performance boost. In this case the boost gets performance almost back to the full 32-bit performance level. The difference is due to the Dhrystone benchmark using integer (32-bit) global data which is still being stored in 16-bit wide memory.

## Slide 44: The ARM Register Set
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
FIQ
IRQ
SVC
Undef
Abort
User Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
FIQ
IRQ
SVC
Undef
Abort
r0
r1
r2
r3
r4
r5
r6
r7
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
IRQ
SVC
Undef
Abort
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
FIQ Mode
IRQ Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
FIQ
SVC
Undef
Abort
r13 (sp)
r14 (lr)
Undef Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
FIQ
IRQ
SVC
Abort
r13 (sp)
r14 (lr)
SVC Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
FIQ
IRQ
Undef
Abort
r13 (sp)
r14 (lr)
Abort Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
FIQ
IRQ
SVC
Undef
r13 (sp)
r14 (lr)
Notes: This animated slide shows the way that the banking of registers works. On the left the currently visible set of registers are shown for a particular mode.
On the right are the registers that are banked out whilst in that mode.
Each key press will switch mode:
user -> FIQ ->user -> IRQ -> user ->SVC -> User -> Undef -> User -> Abort and then back to user.
The following slide then shows this in a more static way that is more useful for reference

## Slide 45: Register Organization Summary
User mode r0-r7, r15, and cpsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
FIQ
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
r15 (pc)
cpsr
r0
r1
r2
r3
r4
r5
r6
r7
User
r13 (sp)
r14 (lr)
spsr
IRQ
User mode r0-r12, r15, and cpsr
r13 (sp)
r14 (lr)
spsr
Undef
User mode r0-r12, r15, and cpsr
r13 (sp)
r14 (lr)
spsr
SVC
User mode r0-r12, r15, and cpsr
r13 (sp)
r14 (lr)
spsr
Abort
User mode r0-r12, r15, and cpsr
Thumb state
High registers
Note: System mode uses the User mode register set
Thumb state
Low registers
Notes: This slide shows the registers visible in each mode - basically in a more static fashion than the previous animated slide that is more useful for reference.
The main point to state here is the splitting of the registers in Thumb state into Low and High registers.
ARM register banking is the minimum necessary for fast handling of overlapping exceptions of different types (e.g. ABORT during SWI during IRQ). For nested exceptions of the same type (e.g. re-entrant interrupts) some additional pushing of registers to the stack is required.

## Slide 46: Program Status Registers
Condition code flags
  N = Negative result from ALU
  Z = Zero result from ALU
  C = ALU operation Carry out
  V = ALU operation oVerflowed
Sticky Overflow flag - Q flag
  Architecture 5TE/J only
  Indicates if saturation has occurred
J bit
  Architecture 5TEJ only
  J = 1: Processor in Jazelle state
Interrupt Disable bits.
  I = 1: Disables the IRQ.
  F = 1: Disables the FIQ.
T Bit
  Architecture xT only
  T = 0: Processor in ARM state
  T = 1: Processor in Thumb state
Mode bits
  Specify the processor mode
27
31
N Z C V Q
28
6
7
I F T mode
16
23
8
15
5
4
0
24
f
s
x
c
U n d e f i n e d
J
Notes: Green psr bits are only in certain versions of the ARM architecture
ALU status flags (set if "S" bit set, implied in Thumb state).
Sticky overflow flag (Q flag) is set either when
  saturation occurs during QADD, QDADD, QSUB or QDSUB, or
  the result of SMLAxy or SMLAWx overflows 32-bits
Once flag has been set can not be modified by one of the above instructions and must write to CPSR using MSR instruction to cleared
PSRs split into four 8-bit fields that can be individually written:
Control (c) bits 0-7
Extension (x) bits 8-15 Reserved for future use
Status (s) bits 16-23 Reserved for future use
Flags (f) bits 24-31
Bits that are reserved for future use should not be modified by current software. Typically, a read-modify-write strategy should be used to update the value of a status register to ensure future compatibility. Note that the T/J bits in the CPSR should never be changed directly by writing to the PSR (use the BX/BXJ instruction to change state instead).
However, in cases where the processor state is known in advance (e.g. on reset, following an interrupt, or some other exception), an immediate value may be written directly into the status registers, to change only specific bits (e.g. to change mode).
New ARM V6 bits now shown.

## Slide 47: Interrupts and Exceptions
External devices like Timer, USB interface, keyboard, mouse, audio input needs attention of the processor
Some internal events may also want to draw processor’s attention
Interrupts and exceptions are special kinds of control transfer, which means that they alter the normal program flow to handle external events or to report errors or exceptional conditions

## Slide 48: Types of Interrupts and Exceptions
IRQ (Normal Interrupt)
FIQ (Fast Interrupt)
Reset
Undefined Instruction
Software Interrupt (SWI)
Prefetch abort (Instruction fetch memory abort)
Data abort (Data access memory abort)

## Slide 49: Exception Priority
Reset
Data Abort
FIQ
IRQ
Prefetch Abort
SWI
Undefined Instruction
Highest
Lowest

## Slide 50: Processor Modes
The ARM has seven basic operating modes:
  User : unprivileged mode under which most tasks run
  FIQ : entered when a high priority (fast) interrupt is raised
  IRQ : entered when a low priority (normal) interrupt is raised
  Supervisor : entered on reset and when a Software Interrupt instruction is
  executed
  Abort : used to handle memory access violations
  Undef : used to handle undefined instructions
  System : privileged mode using the same registers as user mode
Notes: The Programmers Model can be split into two elements - first of all, the processor modes and secondly, the processor registers. So let’s start by looking at the modes.
Now the typical application will run in an unprivileged mode know as “User” mode, whereas the various exception types will be dealt with in one of the privileged modes : Fast Interrupt, Supervisor, Abort, Normal Interrupt and Undefined (and we will look at what causes each of the exceptions later on).
NB - spell out the word FIQ, otherwise you are saying something rude in German!
One question here is what is the difference between the privileged and unprivileged modes? Well in reality very little really - the ARM core has an output signal (nTRANS on ARM7TDMI, InTRANS, DnTRANS on 9, or encoded as part of HPROT or BPROT in AMBA) which indicates whether the current mode is privileged or unprivileged, and this can be used, for instance, by a memory controller to only allow IO access in a privileged mode. In addition some operations are only permitted in a privileged mode, such as directly changing the mode and enabling of interrupts.
All current ARM cores implement system mode (added in architecture v4). This is simply a privileged version of user mode. Important for re-entrant exceptions because no exceptions can cause system mode to be entered.