## Slide 1: Module 17 - 18
Superscalar Processors

## Slide 2: Outline
Issues in Pipelining (understanding the rules of the game!)
  Data Dependency / Hazard
  Structural Dependency / Hazard
  Control Dependency / Hazard
ILP, LLP
Branch Prediction and Speculation
Complex pipelining
Superscalar or VLIW?
  In order and out of order (issue, execution and retirement)

## Slide 3: Overview of Techniques used for reducing stalls
Technique | Target
ISA based techniques | Control hazard stalls
Forwarding and Bypassing | Potential data hazard stalls
Delayed Branches | Control hazard stalls
Dynamic Scheduling | Data hazard stalls from true dependence
Dynamic Scheduling with renaming | Data hazard stalls & name dependencies stalls
Dynamic Branch Prediction | Control hazard stalls
Multiple Instruction per cycle | Ideal CPI
Speculation | Data hazard and Control hazard stalls
Loop Unrolling | Control hazard stalls
Compiler dependence analysis | Ideal CPI, Data hazard stalls
Software pipelining, trace scheduling | Ideal CPI, Data hazard stalls

## Slide 4: Getting CPI below 1…
CPI ≥ 1 if issue only 1 instruction every clock cycle
Multiple-issue processors come in 3 types:
  Statically-scheduled superscalar processors,
  Dynamically-scheduled superscalar processors
  Dynamically scheduled with speculation, and
  VLIW (very long instruction word) processors

## Slide 5: ILP
Instruction-Level Parallelism (ILP): overlap the execution of instructions to improve performance keeping in mind the condition mentioned in the previous slide.
2 approaches to exploit ILP:
  Dynamic Scheduling: Rely on hardware to help discover and exploit the parallelism dynamically.
  Static scheduling: Rely on software technology to find parallelism, statically at compile-time.
It should be noted that scope of parallelism within a basic block is quite small.

## Slide 6: Superscalar Vs VLIW
Superscalar:
  varying no. instructions/cycle (1 to 8), scheduled by compiler or by HW (Tomasulo)
  Qualcomm Scorpion, Krait, TI OMAP4, NVIDIA Tegra 2/3, Cortex A9, Intel Medfield
  A superscalar architecture is one in which several instructions can be initiated simultaneously and executed independently.
Very Long Instruction Words VLIW:
  VLIW processors, in contrast, issue a fixed number of instructions formatted either as one large instruction or as a fixed instruction packet with the parallelism among instructions explicitly indicated by the instruction

## Slide 7: Superscalar vs. VLIW
Which scheduling technique is better? Dynamic? Static?
Superscalar way: Let us build some hardware to take care of instruction scheduling.
VLIW: Let the compiler take care of the same.
Advantage of Superscalar: Uses existing ISA, hence compatible with legacy code.
VLIW: Not so…

## Slide 8: Some Complication…
Pipelines with multiple execution units…
Up to three instructions can simultaneously occupy the execution stage
Delay of each execution unit may be different.
Most modern Application processors have such “deep pipeline” structure
Fetch
1
Fetch
2
Decode
Issue
Shift
ALU
Saturate
Write
back
MAC
1
MAC
2
MAC
3
Address
Data
Cache
1
Data
Cache
2

## Slide 9: Dynamic Scheduling
Why do we need this stage?
Is the required function unit available?
Is the input data available? => RAW?
Is it safe to write the destination? => WAR? WAW?
Is there a structural conflict at the WB stage?
Fetch
1
Fetch
2
Decode
Issue
Shift
ALU
Saturate
Write
back
MAC
1
MAC
2
MAC
3
Address
Data
Cache
1
Data
Cache
2

## Slide 10: In order and Out of Order (OOO) issue
In Order instruction issue is simple.
Can we change the order of instruction execution? Dynamic scheduling implies OoO execution and OoO completion
Creates the possibility of WAR and WAW hazards…
Implementation…
  Issue stage buffer holds multiple instructions waiting to issue
  Decode adds next instruction to buffer if there is space and the instruction does not cause a WAR or WAW hazard.
  Any instruction in buffer called as the Reservation station (RS) whose RAW hazards are satisfied can be issued. On a write back (WB), new instructions may get enabled.

## Slide 11: Superscalar
2 types of superscalar processors issue varying numbers of instructions per clock. ARM 11 and Cortex Ax family uses dual issue instruction format.
  use in-order execution if they are statically scheduled, or
  out-of-order execution if they are dynamically scheduled
Imprecise Exception…

## Slide 12: Things to consider in Multiple Issue
issue packet: group of instructions from fetch unit that could potentially issue in 1 clock
  If instruction causes structural hazard or a data hazard either due to earlier instruction in execution or to earlier instruction in issue packet, then instruction does not issue
  0 to N instruction issues per clock cycle, for N-issue
Performing issue checks in 1 cycle could limit clock cycle time: O(n2-n) comparisons
  => issue stage usually split and pipelined
  1st stage decides how many instructions from within this packet can issue, 2nd stage examines hazards among selected instructions and those already been issued
  => higher branch penalties => prediction accuracy important

## Slide 13: Tomasulo Organization (a technique for dynamic scheduling)
adders
Add1
Add2
Add3
multipliers
Mult1
Mult2
From Mem
Registers
Reservation
Stations
Common Data Bus (CDB)
To Mem
Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 14: Reservation Station Components
Op: Operation to perform in the unit (e.g., + or –)
Vj, Vk: Value of Source operands
  Store buffers has V field, result to be stored
Qj, Qk: Reservation stations producing source registers (value to be written)
  Note: Qj,Qk=0 => ready
  Store buffers only have Qi for RS producing result
Busy: Indicates reservation station or FU is busy
Register result status—Indicates which functional unit will write each register, if one exists. Blank when no pending instructions that will write that register.
Notes: What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 15: Three Stages of Tomasulo Algorithm
1. Issue—get instruction from Op Queue
  If reservation station free (no structural hazard), control issues instr & sends operands (renames registers).
2. Execute—operate on operands (EX)
  When both operands ready then execute; if not ready, watch Common Data Bus for result
3. Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting units; mark reservation station available
Normal data bus: data + destination (“go to” bus)
Common data bus: data + source (“come from” bus)
  64 bits of data + 4 bits of Functional Unit source address
  Write if matches expected Functional Unit (produces result)
  Does the broadcast
Example speed:
3 clocks for Fl. pt. +,-; 10 for * ; 40 clks for /

## Slide 16: Tomasulo Example
Clock cycle counter
FU count
down
Instruction stream
3 Load/Buffers
3 Adder R.S.
2 Mult R.S.

## Slide 17: Tomasulo Example Cycle 1

## Slide 18: Tomasulo Example Cycle 2
Note: Can have multiple loads outstanding

## Slide 19: Tomasulo Example Cycle 3
Note: registers names are removed (“renamed”) in Reservation Stations; MUL issued
Load1 completing; what is waiting for Load1?

## Slide 20: Tomasulo Example Cycle 4
Load2 completing; what is waiting for Load2?

## Slide 21: Tomasulo Example Cycle 5
Timer starts down for Add1, Mult1

## Slide 22: Tomasulo Example Cycle 6
Issue ADD here despite name dependency on R6?

## Slide 23: Tomasulo Example Cycle 7
Add1 (SUB) completing; what is waiting for it?

## Slide 24: Tomasulo Example Cycle 8

## Slide 25: Tomasulo Example Cycle 9

## Slide 26: Tomasulo Example Cycle 10
Add2 (ADD) completing; what is waiting for it?

## Slide 27: Tomasulo Example Cycle 11
Write result of ADD here?
All quick instructions complete in this cycle!

## Slide 28: Tomasulo Example Cycle 12

## Slide 29: Tomasulo Example Cycle 13

## Slide 30: Tomasulo Example Cycle 14

## Slide 31: Tomasulo Example Cycle 15
Mult1 (MUL) completing; what is waiting for it?

## Slide 32: Tomasulo Example Cycle 16
Just waiting for Mult2 (DIV) to complete

## Slide 33: Loop Level Parallelism (LLP)
In a Basic Block, the scope of ILP is quite small.
To obtain substantial performance enhancements, we must exploit ILP across multiple basic blocks.
Simplest LLP is Loop unrolling. Limited only by the loop size and available registers.
Consider following example; assume R2 contains the scalar value s, [R1] is the address of the element in the array with the highest address, for simplicity we assume that the element with the lowest address is at 0
        Loop: LDR R0, [R1] ; R0=array element
        ADD R4, R0, R2 ; Increment R4 by
        R0 + [R2]
        STR R4, [R1] ; store result
SUB R1, R1, #4 ; decrement pointer
by 4 bytes
BNE R1, Loop ; branch if R1 != 0
Useful work
Overhead
for (i = 1; i <= 1000, i++)
x[i] = x[i} + s

## Slide 34: Loop without scheduling…
Suppose LDR and BNEZ takes two cycles each. Without any scheduling, the loop would look like;
It would require 7 cycles per iteration
Can we improve the performance by Static scheduling?
        Loop: LDR R0, [R1] 1
        stall 2
        ADD R4, R0, R2 3
        STR R4, [R1] 4
        SUB R1, R1, #4 5
        BNE R1, Loop 6
        Stall 7

## Slide 35: Loop with Static Scheduling…
Is this possible? Out of Order Execution and Out of Order Completion…
Smart compiler has provided an improvement of 2 cycles…
Still, we do useful work only in three cycles (LDR, ADD and STR), rest two cycles are the loop overhead (SUB and BNE). Can we still do better?
        Loop: LDR R0, [R1] 1
        SUB R1, R1, #4 2
        ADD R4, R0, R2 3
        BNE R1, Loop 4
        STR R4, [R1 , #4 ] 5

## Slide 36: Loop unrolling
Loop unrolling means, replicate the loop body several times and adjust the termination code. The idea is to get more number of instructions within the loop relative to the loop overhead
Loop LDR R0, [R1]
        ADD R4, R0, R2
        STR R4, [R1]
        LDR R6, [R1] , # -4
        ADD R8, R6, R2
        STR R8, [R1], # -4
        LDR R10, [R1], # -8
        ADD R12, R10, R2
        STR R12, [R1], # -8
        LDR R14, [R1], # -12
        ADD R16, R14, R2
        STR R16, [R1] , #-12
        SUB R1, R1, #16
        BNE R1, Loop
Removed BNZ and SUB
Removed BNZ and SUB
Removed BNZ and SUB
Not Much Benefit in Loop
unrolling alone. ~ 5 cycles
per loop

## Slide 37: Loop unrolling + Scheduling
Loop LDR R0, [R1]
LDR R6, [R1] , # -4
LDR R10, [R1], # -8
LDR R14, [R1], # -12
ADD R4, R0, R2
ADD R8, R6, R2
ADD R12, R10, R2
ADD R16, R14, R2
STR R4, [R1]
STR R8, [R1], # -4
SUB R1, R1, #16
STR R12, [R1], # 8 ; 8 – 16 = -8
BNE R1, Loop
STR R16, [R1] , # 4
3.5 cycles per loop!

## Slide 38: Software Pipelining and Trace Scheduling
Iteration 0
Iteration 1
Iteration 2
Iteration 3
Iteration 4

## Slide 39: Example of Software Pipelining
Loop: LDR R0, [R1]
ADD R4, R0 R2
STR R4, [R1]
SUB R1, R1, #4
BNE R1, Loop
Iteration i: LDR R0, [R1]
ADD R4, R0, R2
STR R4, [R1]
Iteration i + 1: LDR R0, [R1]
ADD R4, R0, R2
STR R4, [R1]
Iteration i + 2: LDR R0, [R1]
ADD R4, R0, R2
STR R4, [R1]

## Slide 40: Speculation….
What is Speculation
  Idea is to overcome control dependence by speculating on the outcome of the branches and executing the program as if our guesses were correct
Speculation is going one step ahead of “Dynamic Speculation with branch prediction” where the guessed instructions are only fetched and issued but not executed
Instruction execution with speculation is a four step process;
  Issue
  Execute
  Write Result in the Reorder Buffer (ROB)
  Commit
How much should one speculate? Over multiple branches?

## Slide 41: Trace Scheduling
Parallelism across IF branches vs. LOOP branches
Two steps:
  Trace Selection
  Find likely sequence of basic blocks (trace)
  of (statically predicted or profile predicted)
  long sequence of straight-line code
– Trace Compaction
  Squeeze trace into few VLIW instructions
  Need bookkeeping code in case prediction is wrong
Compiler undo bad guess (discards values in registers)
Subtle compiler bugs mean wrong answer vs. poorer performance; no hardware interlocks

## Slide 42: How much to speculate?
Speculation Pro: uncover events that would otherwise
stall the pipeline (cache misses)
Speculation Con: speculate costly if exceptional event
occurs when speculation was incorrect
Typical solution: speculation allows only low-cost
exceptional events (1st-level cache miss)
When expensive exceptional event occurs, (2nd-level cache miss or TLB miss) processor waits until the instruction causing event is no longer speculative before handling the event
Assuming single branch per cycle: future may speculate across multiple branches!

## Slide 43: Architecture Comparison
 | Cortex A9 | Cortex A15 | Qualcomm Scorpion | Qualcomm Krait
Decode Width | 2 wide | - | 2 wide | 3 wide
Pipeline Depth | 8 | 14 | 10 | 11
Issue Width | 2 | 8 (?) | 3 | 4
OoO execution | Y | Y | Partial | Y
FPU | Optional VFPv3-D16 Pipelined | VFPv3 Pipelined | VFPv3 Pipelined | VFPv3 Pipelined
NEON | Optional MPE, 64 bit | Y | Y 128 bit | Y 128 bit
Process Technology | 40 | 32/28 | 40 | 28
Clock Speed | 1-1.2 GHz | 1.5 – 2.5 GHz | 1.2GHz | 1.5GHz

## Slide 44: Next session…
Limits on ILP…
What is the alternative to decrease CPI?
Software holds the key to future performance enhancement…