## Slide 1: Mid-term 1 result analysis
Highest Marks: 42.5
Below 20 Marks: 254 students
Below 10 Marks: 105 students
0 Marks: 12 students
Average: 14 Marks

## Slide 2: Important Announcement
From Monday, 23rd Sept, 2019, there would be no regular lectures in LT-3 till Thursday, 26th Sept
There will be a tutorial session in CEP 103 from 4:00pm to 5:30pm
You need to attend it according to your assigned Lab group day
To take advantage of the tutorial session, you need to come prepared

## Slide 3: Art of Branch prediction A practice problem
EL 426

## Slide 4
0x100 INITIAL: R1 = MEM[R2+0]
0x104 If (R1 > 0) goto DEST // Branch 1
0x108 R4 = R4+1, R6 = R6 + R1
0x10C R3 = R4 + R6
0x110 R6 = R6/2
0x114 R4= R4 + R6
0x118 R5 = R4*R6
0x11C R2 = R2 + 4
0x120 DEST: R6 = R6/3
0x124 if(R4 < 50000) goto INITIAL // Branch 2
Note that 0x100 = 0001 0000 0000. Last two bits are word offset
In the first case of predictor 1, there are 8 entries starting from 000 to 111. PC address of each branch would be referred to by last three bits of PC – disregarding the offset bits.

## Slide 5
Possible mapping of each branch address in the 8 entry branch prediction table
000 INITIAL: R1 = MEM[R2+0]
001 If (R1 > 0) goto DEST // Branch 1
010 R4 = R4+1, R6 = R6 + R1
011 R3 = R4 + R6
100 R6 = R6/2
101 R4= R4 + R6
110 R5 = R4*R6
111 R2 = R2 + 4
000 DEST: R6 = R6/3
001 if(R4 < 50000) goto INITIAL // Branch 2

## Slide 6
You are now to consider 2 branch predictors:
Predictor 1: A PC-based predictor with 8 entries each a 1 bit predictor.
Predictor 2: A local pattern history predictor. The BHT has 16 entries, each with 2 bits of history. The predictors are each 1 bit.

## Slide 7
Case 1: The data loaded from memory is 1 the first time, 0 the second, 1 the third, 0 the forth and follows that pattern forever (1, 0, 1, 0, 1, 0, etc.)
Case 2: The data loaded from memory is 0 the first time, -1 the second, -1 the third, -1 the forth and follows that pattern forever (0, -1 -1, -1, 0, -1, -1, -1, etc.)
Case 3: The data loaded is (1, 0, -1, 1, 0, -1, 1, 0, -1, etc.)
 | Case 1 |  | Case 2 |  | Case 3 | 
 | Predictor 1 | Predictor 2 | Predictor 1 | Predictor 2 | Predictor 1 | Predictor 2
Branch 1 |  |  |  |  |  | 
Branch 2 |  |  |  |  |  |