## Slide 1: Implementation Issues The Concepts Module 4 - 9
Notes: v10: 28/04/03, Chris Shore
slide 4: added China to text (already on graphic). Updated employee count and geographical distribution.
slide 19: added V6
slides 32: Imported from RV Overview to replace original ADS slide.
slide 33: New general debug architecture diagram
slide 34: new product montage (crib in notes)
slide 35: New question about embedded trace.
v09: 19/11/02, Chris Shore
slides 6-8: New slides showing IP deployment (imported from 926 core module)
v08: 08/02, Rob Levy
- Style update, black & white view amended
v07: 12/01, CJS
Main changes:
- ARM Development Boards slide removed (now in Debug Solutions module)
- Register set slides re-ordered so that the animated graphic comes first
- slide 12: Q bit in v5TEJ as well as v5TE
- slide 14: CPSR changes rephrased slightly
- slide 16: reference to v5T removed.
- slide 27: EASY/Micropack replaced with ADK/ACT
- slide 30: Trace slide updated

## Slide 2: Qualcomm Announcement
Qualcomm Krait (1.5 GHz) has 11 stage pipeline, quadruple issue, out of order (OoO), speculating, superscalar, multi-core and ARM 7A compliant architecture
HTC One-S would be the first phone in the market with Krait processor (S4 /MSM 8960 chipset)
(as announced in the MWC 2012)

## Slide 3: Computing Environment
Computer Architecture
Compiler Techniques
Operating system
&
Software Techniques
Implementation
Instruction Set Architecture
Loop Transformation &
Procedure inlining
Register Allocation
Local and Global Optimization &
Pipeline Scheduling

## Slide 4: The basics…
Non-pipelined processor.
Assume that each operation
takes 75ns
Pipelined processor with 5 stages
Assume each stage takes 17ns.
1st Output 75ns
2nd Output 150ns
3rd Output 225ns
… … ….
1st Output 85ns
2nd Output 102ns
3rd Output 119ns
F
F
D
E
M
W
Pipe-lining is a good idea as long as we manage to keep it filled…
Processor A
Processor B
Proc A Speed = 13.33MHz
Proc. B Speed = 58.82MHz

## Slide 5: Outline
Issues in Pipelining (understanding the rules of the game!)
  Data Dependency / Hazard
  Structural Dependency / Hazard
  Control Dependency / Hazard
ILP, LLP
Branch Prediction and Speculation
Complex pipelining
Superscalar or VLIW?
  In order and out of order (issue, execution and retirement)

## Slide 6: Single issue pipeline architecture
In such single issue pipeline, the upper limit of performance is 1 clock cycle per instruction (CPI)
Many road blocks in achieving the CPI = 1
  Data Flow related issues
  Limitation of resources
  Branches
Instruction
Fetch
Shift + ALU
Memory
Access
Reg
Write
Reg
Read
Reg
Decode
FETCH
DECODE
EXECUTE
MEMORY
WRITE

## Slide 7: Data Dependencies…
Dependences are the property of a program (Data flow)
Date Dependence conveys
  Order in which results must be calculated
  Potential for a hazard, but actual hazard and length of any stall is a property of the pipeline
I: ADD R1,R2,R3
J: SUB R4,R1,R3
  Upper bound on exploitable instruction level parallelism
Dependencies that flow through memory locations are difficult to detect eg [R1, #32] and [R4, #8] might be pointing to the same memory location

## Slide 8: Data Hazard
RAW Hazard (Read after Write) – Due to Data Dependency
Instruction J tries to read operand before Instr. I writes it I: ADD R1,R2,R3
J: SUB R4,R1,R3
Caused by a “Dependence” (in compiler nomenclature).
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
I: add r1,r2,r3
J: sub r4,r1,r3
Value of R1 generated
Value of R1 needed

## Slide 9: Solutions
Reg
ALU
DMem
Ifetch
Reg
Reg
Ifetch
ALU
DMem
Reg
Bubble
Bubble
Wait till the Value of R1
Becomes available
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Do Data Forwarding

## Slide 10
Data forwarding can not solve all the problems (Load interlock)
Solution: Wait and your problems will go away!
Reg
Ifetch
ALU
DMem
Reg
Bubble
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
LDR R1, [R2]
SUB R4,R1,R6
LDR R1, [R2]
SUB R4,R1,R6
Time (clock cycles)

## Slide 11: Data Hazard (continued)
WAR Hazard (Write after Read) – Due to Anti-dependence
Instr I writes operand before Instr J reads it
No problem of WAR hazard in simple “in-line” pipelining
Will cause a problem in multiple issue, out of order execution
I: SUB R4,R1,R3
J: add R1,R2,R3

## Slide 12
WAW hazard (Write after Write) – Due to Output dependence
Instr J writes operand before Instr I writes it
No possibility of WAW hazard in simple “in-line” pipelining
Will become an issue when out of order execution is allowed
I: SUB R1,R4,R3
J: ADD R1,R2,R3

## Slide 13: Name Dependence
Two instructions use the same name but no flow of information
Not a true data dependence, but is a problem when reordering instructions
  Antidependence: instruction j writes a register or memory location that instruction i reads
    Initial ordering (i before j) must be preserved
  Output dependence: instruction i and instruction j write the same register or memory location
    Ordering must be preserved
To resolve, use register renaming technique

## Slide 14: Structural hazard
Hardware can not support the given combination of instructions. If there is just one memory system for instruction and data then structural hazard may occur.
For complex pipeline with split execution unit (many functional units) structural hazard may occur.
Solution? Wait….

## Slide 15: Control Hazard
Ordering of an instruction i with respect to a branch instruction
  Instruction control dependent on a branch cannot be moved before the branch so that its execution is no longer controlled by the branch
  An instruction not control dependent on a branch cannot be moved after the branch so that its execution is controlled by the branch
  If some how we can predict the behavior of branch or even better - eliminate them, then code execution would be very fast.

## Slide 16: Final word on dependences
Preserving Control dependence is a simple and effective way of maintaining program correctness
However, Control dependence is not a fundamental performance limit
Control dependence can be violated if;
  Exception behavior &
  Data Flow
are maintained
Preserving the Exception behavior means that any change in the order of the instruction execution should not change how exception are raised in the program

## Slide 17: So what happens to the pipeline CPI?
Pipeline CPI = Ideal CPI + structural stalls + RAW stalls +
WAR stalls + WAW stalls + Control stalls
What can we do about these stall penalties?

## Slide 18: Overview of Techniques used for reducing stalls
Technique | Target
ISA based techniques | Control hazard stalls
Forwarding and Bypassing | Potential data hazard stalls
Delayed Branches | Control hazard stalls
Dynamic Scheduling | Data hazard stalls from true dependence
Dynamic Scheduling with renaming | Data hazard stalls & name dependencies stalls
Dynamic Branch Prediction | Control hazard stalls
Multiple Instruction per cycle | Ideal CPI
Speculation | Data hazard and Control hazard stalls
Loop Unrolling | Control hazard stalls
Compiler dependence analysis | Ideal CPI, Data hazard stalls
Software pipelining, trace scheduling | Ideal CPI, Data hazard stalls

## Slide 19: ISA based solution…
A cleaver solution has been created to address some of the control stalls
In ARM instruction set, almost every instruction may be conditionally executed.
There are 16 possible condition starting from “Always” to “Never” (which is not used. Code reserved for future expansion).
(conventional way) (ARM way)
  CMP R3,#0 CMP R3,#0
  BEQ SKIP ADDNE R0,R1,R2 ADD R0,R1,R2
  Skip
The conventional way could waste up to three cycles!

## Slide 20: Another example…
Take a look at following C
code
int gcd (int i, int j)
{
while (i != 0)
{
if (i > j)
i -= j;
else
j -= i;
}
return i;
}
Equivalent ARM assembly language code would be
Loop CMP Ri, 0 ; set condition
; “NE” if (i != 0)
; “GT” if (i > j)
; “LT” if (i < j)
SUBGT Ri, Ri, Rj ; if GT, i = i – j
SUBLT Ri, Rj, Ri ; if LT, j = j – i
BNE Loop
This code avoids branches around “then” and “else” clause.

## Slide 21: Branch Prediction
If branches can be predicted (Taken or Not-Taken) with high percentage, then we can reduce stalls by fetching the “target instruction” earlier
When is information about branches gathered/applied?
– When the program is compiled (“compile-time” or Static)
– As the program is being executed (“dynamic”)
– When a “training run” of the program is executed
(“profile-based”) … compile – profile - compile
Prediction is a gamble!
Performance gain = ƒ(accuracy, cost of misprediction)

## Slide 22: Static Branch Prediction Techniques
Static Branch prediction.
Simple to implement. Not much hardware required.
Can be used as a fall through mechanism.
  Predict always not taken
  Predict always taken
  Backward branch predict taken, forward
  branch predict not taken.

## Slide 23: Dynamic Branch Prediction
Dynamic Branch Prediction Scheme.
  Learning based on the past behavior.
Temporal correlation
  The way a branch resolves may be a good predictor of the way it will resolve at the next execution
Spatial correlation
  Several branches may resolve in a highly correlated manner (a preferred path of execution)

## Slide 24: Dynamic Branch Prediction Schemes
1-bit Branch-Prediction Buffer
2-bit Branch-Prediction Buffer
Correlating Branch Prediction Buffer
Tournament Branch Predictor
Branch Target Buffer
Integrated Instruction Fetch Units
Return Address Predictors

## Slide 25: Dynamic Branch Prediction (Contd.)
Take advantage of the knowledge of temporal correlation.
Use Branch prediction buffer
Example; Consider 1 bit prediction buffer; 0 = branch not taken and 1 = branch taken
Suppose we have to take this loop 100 times, how will one bit branch prediction scheme perform?
loop | CMP | Ri, 0 | ; Set Condition ; “NE” if (i != 0) ; “GT” if (i > j) ; “LT” if (i < j)
 | SUBGT | Ri, Ri, Rj | ; if GT, i = i - j
 | SUBLT | Ri, Rj, Ri | ; if LT, j = j – i
 | BNE | loop | 

## Slide 26: One Bit Branch Prediction Counter
Branch History Table (BHT): Lower bits of PC address index table of 1-bit values
  Says whether or not branch taken last time ( T-Taken, NT Not taken )
  No full address check (saves HW, but may be wrong)
In a given single loop, One bit branch prediction counter will provide two wrong predictions;
  First time through the loop, when it predicts exit instead of looping
  Last time through the loop, when it predicts looping instead of exit
How about using a two bit counter?

## Slide 27: Dynamic Branch Prediction (2 bit counter)
Can we better the performance ?
Use two bit branch prediction buffer… i.e. change prediction only when the prediction is wrong twice.
T
T
NT
NT
Predict Taken
Predict Not
Taken
Predict Taken
Predict Not
Taken
T
NT
T
NT
11
10
00
01

## Slide 28: Can we do better with n-bit counter?
n-bit predictor:
  counter can hold values between 0 and
  predict taken when value is greater than or equal to half of maximum value:
  The counter is incremented on each taken branch
  and decremented on each not taken branch
Not much benefit over 2 bit counter…

## Slide 29: Dynamic Branch Prediction (Contd.)
How about Spatial correlation?
Consider following example…
If first condition fails, second condition also fails
Global History Buffer (GHB), records the direction of the last N branches executed by the processor
if (x[i] < 7) then
y += 1;
if (x[i] < 5) then
c -= 4;

## Slide 30: Correlating Branch predictor
Hypothesis: Previous 2-bit predictor schemes use only the recent behavior of a single branch to predict the future behavior of that branch
But branches are correlated; that is, behavior of recently-executed branches affects prediction of current branch
if (aa == 2)
aa = 0; #Branch 1
if (bb == 2)
bb = 0; #Branch 2
if (aa! = bb) { #Branch 3
Clearly branch #3 depends on outcome of #1 and #2
Prediction must be a function of own branch as well as recent outcomes of other branches

## Slide 31: Correlating Branch predictor (cont.)
Idea: record m most recently executed branches as taken or not taken, and use that pattern to select the proper n-bit branch history table
In general, (m,n) predictor means record last m branches to select between 2m history tables, each with n-bit counters
  Thus, old 2-bit BHT is a (0,2) predictor
Global Branch History: m-bit shift register keeping T/NT status of last m branches
Each entry in table has m n-bit predictors

## Slide 32: Correlating Branches
(2,2) predictor
Behavior of recent branches(global branch history) is used to select between four predictions of next branch, updating just that prediction
Branch address(low-order bits)
2-bits per branch predictor
Prediction
2-bit global branch history
4 bits
NN
NT
TN
TT
N
T
SHIFT

## Slide 33: Tournament Predictors
Tournament Predictors are the most popular form of Multilevel branch predictors
Use 2-bit saturating counter per branch to choose between two different predictors
Use choice predictor to choose between global and local predictors
n/m means:
n = left predictor value
m = right predictor value
0: Incorrect
1: Correct
Notes: gdhgfdgf

## Slide 34: Branch Target Predictions
We have been looking at the ways to predict direction of branches (Taken/Not-Taken)
It would be beneficial if we could predict the branch address (target address) and fetch it ASAP
– Branch Target Buffer (BTB)
• Branch target buffer (BTB) stores address of the last target location to avoid recomputing
    Useful for conditional/unconditional branches
– Return Address Stack (RAS)
• Useful for procedure returns

## Slide 35: Branch Target Buffer
Global history buffer Only predicts branch direction. Therefore, cannot redirect fetch stream until after branch target is determined. This is no good.
Use Branch Target Buffer along with GHB.
BTB stores PCs the same way as caches
The PC of a branch is sent to the BTB
When a match is found the corresponding Predicted PC is returned
If the branch was predicted taken, instruction fetch continues at the returned predicted PC
Zero cycle unconditional branch and some times zero cycle conditional branch (Branch folding)

## Slide 36: BTB flow chart
Taken
Branch?
Entry found in branch-target buffer?
Send out predicted PC
Is instruction a taken branch?
Send PC to memory and branch-target buffer
Enter branch instruction address and next PC into branch-target buffer
Mispredicted branch, kill fetched instruction; restart fetch at other target; delete entry from target buffer
Normal instruction execution
Branch correctly predicted; continue execution with no stalls
No
Yes
Yes
Yes
No
No
ID
IF
EX

## Slide 37: BTB with GHB
Yes: instruction is branch and use predicted PC as next PC
No: branch not
predicted, proceed normally
(Next PC = PC+4)
Branch PC
Predicted PC
=?
PC of instruction
FETCH
Extra
prediction state
bits

## Slide 38: Price to pay for Misprediction
In a simple “in order” architecture, kill all instructions behind the mispredicted branch.
Fetch from the new PC value.
How about interrupts?

## Slide 39: Return Address Predictors
Procedure returns account for ~85% of indirect jumps (jumps whose address varies at run time). It will then return to many different locations—BTB may not predict accurately,
Therefore, small buffer of Return Addresses=cache of the most recent return addresses
• Like a hardware stack, LIFO
– At Procedure Call => Push Return address onto stack
– Procedure Return => Prediction off of top of stack, Pop it
• RAS tends to work quite well since call depths are typically not large

## Slide 40: Getting CPI below 1…
CPI ≥ 1 if issue only 1 instruction every clock cycle
Multiple-issue processors come in 3 types:
  Statically-scheduled superscalar processors,
  Dynamically-scheduled superscalar processors
  Dynamically scheduled with speculation, and
  VLIW (very long instruction word) processors

## Slide 41: ILP
Instruction-Level Parallelism (ILP): overlap the execution of instructions to improve performance keeping in mind the condition mentioned in the previous slide.
2 approaches to exploit ILP:
  Dynamic Scheduling: Rely on hardware to help discover and exploit the parallelism dynamically.
  Static scheduling: Rely on software technology to find parallelism, statically at compile-time.
It should be noted that scope of parallelism within a basic block is quite small.

## Slide 42: Superscalar Vs VLIW
Superscalar:
  varying no. instructions/cycle (1 to 8), scheduled by compiler or by HW (Tomasulo)
  Qualcomm Scorpion, Krait, TI OMAP4, NVIDIA Tegra 2/3, Cortex A9, Intel Medfield
  A superscalar architecture is one in which several instructions can be initiated simultaneously and executed independently.
Very Long Instruction Words VLIW:
  VLIW processors, in contrast, issue a fixed number of instructions formatted either as one large instruction or as a fixed instruction packet with the parallelism among instructions explicitly indicated by the instruction

## Slide 43: Superscalar vs. VLIW
Which scheduling technique is better? Dynamic? Static?
Superscalar way: Let us build some hardware to take care of instruction scheduling.
VLIW: Let the compiler take care of the same.
Advantage of Superscalar: Uses existing ISA, hence compatible with legacy code.
VLIW: Not so…

## Slide 44: Some Complication…
Pipelines with multiple execution units…
Up to three instructions can simultaneously occupy the execution stage
Delay of each execution unit may be different.
Most modern Application processors have such “deep pipeline” structure
Fetch
1
Fetch
2
Decode
Issue
Shift
ALU
Saturate
Write
back
MAC
1
MAC
2
MAC
3
Address
Data
Cache
1
Data
Cache
2

## Slide 45: Dynamic Scheduling
Why do we need this stage?
Is the required function unit available?
Is the input data available? => RAW?
Is it safe to write the destination? => WAR? WAW?
Is there a structural conflict at the WB stage?
Fetch
1
Fetch
2
Decode
Issue
Shift
ALU
Saturate
Write
back
MAC
1
MAC
2
MAC
3
Address
Data
Cache
1
Data
Cache
2

## Slide 46: In order and Out of Order (OOO) issue
In Order instruction issue is simple.
Can we change the order of instruction execution? Dynamic scheduling implies OoO execution and OoO completion
Creates the possibility of WAR and WAW hazards…
Implementation…
  Issue stage buffer holds multiple instructions waiting to issue
  Decode adds next instruction to buffer if there is space and the instruction does not cause a WAR or WAW hazard.
  Any instruction in buffer called as the Reservation station (RS) whose RAW hazards are satisfied can be issued. On a write back (WB), new instructions may get enabled.

## Slide 47: Superscalar
2 types of superscalar processors issue varying numbers of instructions per clock. ARM 11 and Cortex Ax family uses dual issue instruction format.
  use in-order execution if they are statically scheduled, or
  out-of-order execution if they are dynamically scheduled
Imprecise Exception…

## Slide 48: Things to consider in Multiple Issue
issue packet: group of instructions from fetch unit that could potentially issue in 1 clock
  If instruction causes structural hazard or a data hazard either due to earlier instruction in execution or to earlier instruction in issue packet, then instruction does not issue
  0 to N instruction issues per clock cycle, for N-issue
Performing issue checks in 1 cycle could limit clock cycle time: O(n2-n) comparisons
  => issue stage usually split and pipelined
  1st stage decides how many instructions from within this packet can issue, 2nd stage examines hazards among selected instructions and those already been issued
  => higher branch penalties => prediction accuracy important

## Slide 49: Tomasulo Organization (a technique for dynamic scheduling)
adders
Add1
Add2
Add3
multipliers
Mult1
Mult2
From Mem
Registers
Reservation
Stations
Common Data Bus (CDB)
To Mem
Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 50: Reservation Station Components
Op: Operation to perform in the unit (e.g., + or –)
Vj, Vk: Value of Source operands
  Store buffers has V field, result to be stored
Qj, Qk: Reservation stations producing source registers (value to be written)
  Note: Qj,Qk=0 => ready
  Store buffers only have Qi for RS producing result
Busy: Indicates reservation station or FU is busy
Register result status—Indicates which functional unit will write each register, if one exists. Blank when no pending instructions that will write that register.
Notes: What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 51: Three Stages of Tomasulo Algorithm
1. Issue—get instruction from Op Queue
  If reservation station free (no structural hazard), control issues instr & sends operands (renames registers).
2. Execute—operate on operands (EX)
  When both operands ready then execute; if not ready, watch Common Data Bus for result
3. Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting units; mark reservation station available
Normal data bus: data + destination (“go to” bus)
Common data bus: data + source (“come from” bus)
  64 bits of data + 4 bits of Functional Unit source address
  Write if matches expected Functional Unit (produces result)
  Does the broadcast
Example speed:
3 clocks for Fl. pt. +,-; 10 for * ; 40 clks for /

## Slide 52: Tomasulo Example
Clock cycle counter
FU count
down
Instruction stream
3 Load/Buffers
3 Adder R.S.
2 Mult R.S.

## Slide 53: Tomasulo Example Cycle 1

## Slide 54: Tomasulo Example Cycle 2
Note: Can have multiple loads outstanding

## Slide 55: Tomasulo Example Cycle 3
Note: registers names are removed (“renamed”) in Reservation Stations; MUL issued
Load1 completing; what is waiting for Load1?

## Slide 56: Tomasulo Example Cycle 4
Load2 completing; what is waiting for Load2?

## Slide 57: Tomasulo Example Cycle 5
Timer starts down for Add1, Mult1

## Slide 58: Tomasulo Example Cycle 6
Issue ADD here despite name dependency on R6?

## Slide 59: Tomasulo Example Cycle 7
Add1 (SUB) completing; what is waiting for it?

## Slide 60: Tomasulo Example Cycle 8

## Slide 61: Tomasulo Example Cycle 9

## Slide 62: Tomasulo Example Cycle 10
Add2 (ADD) completing; what is waiting for it?

## Slide 63: Tomasulo Example Cycle 11
Write result of ADD here?
All quick instructions complete in this cycle!

## Slide 64: Tomasulo Example Cycle 12

## Slide 65: Tomasulo Example Cycle 13

## Slide 66: Tomasulo Example Cycle 14

## Slide 67: Tomasulo Example Cycle 15
Mult1 (MUL) completing; what is waiting for it?

## Slide 68: Tomasulo Example Cycle 16
Just waiting for Mult2 (DIV) to complete

## Slide 69: Loop Level Parallelism (LLP)
In a Basic Block, the scope of ILP is quite small.
To obtain substantial performance enhancements, we must exploit ILP across multiple basic blocks.
Simplest LLP is Loop unrolling. Limited only by the loop size and available registers.
Consider following example; assume R2 contains the scalar value s, [R1] is the address of the element in the array with the highest address, for simplicity we assume that the element with the lowest address is at 0
        Loop: LDR R0, [R1] ; R0=array element
        ADD R4, R0, R2 ; Increment R4 by
        R0 + [R2]
        STR R4, [R1] ; store result
SUB R1, R1, #4 ; decrement pointer
by 4 bytes
BNE R1, Loop ; branch if R1 != 0
Useful work
Overhead
for (i = 1; i <= 1000, i++)
x[i] = x[i} + s

## Slide 70: Loop without scheduling…
Suppose LDR and BNEZ takes two cycles each. Without any scheduling, the loop would look like;
It would require 7 cycles per iteration
Can we improve the performance by Static scheduling?
        Loop: LDR R0, [R1] 1
        stall 2
        ADD R4, R0, R2 3
        STR R4, [R1] 4
        SUB R1, R1, #4 5
        BNE R1, Loop 6
        Stall 7

## Slide 71: Loop with Static Scheduling…
Is this possible? Out of Order Execution and Out of Order Completion…
Smart compiler has provided an improvement of 2 cycles…
Still, we do useful work only in three cycles (LDR, ADD and STR), rest two cycles are the loop overhead (SUB and BNE). Can we still do better?
        Loop: LDR R0, [R1] 1
        SUB R1, R1, #4 2
        ADD R4, R0, R2 3
        BNE R1, Loop 4
        STR R4, [R1 , #4 ] 5

## Slide 72: Loop unrolling
Loop unrolling means, replicate the loop body several times and adjust the termination code. The idea is to get more number of instructions within the loop relative to the loop overhead
Loop LDR R0, [R1]
        ADD R4, R0, R2
        STR R4, [R1]
        LDR R6, [R1] , # -4
        ADD R8, R6, R2
        STR R8, [R1], # -4
        LDR R10, [R1], # -8
        ADD R12, R10, R2
        STR R12, [R1], # -8
        LDR R14, [R1], # -12
        ADD R16, R14, R2
        STR R16, [R1] , #-12
        SUB R1, R1, #16
        BNE R1, Loop
Removed BNZ and SUB
Removed BNZ and SUB
Removed BNZ and SUB
Not Much Benefit in Loop
unrolling alone. ~ 5 cycles
per loop

## Slide 73: Loop unrolling + Scheduling
Loop LDR R0, [R1]
LDR R6, [R1] , # -4
LDR R10, [R1], # -8
LDR R14, [R1], # -12
ADD R4, R0, R2
ADD R8, R6, R2
ADD R12, R10, R2
ADD R16, R14, R2
STR R4, [R1]
STR R8, [R1], # -4
SUB R1, R1, #16
STR R12, [R1], # 8 ; 8 – 16 = -8
BNE R1, Loop
STR R16, [R1] , # 4
3.5 cycles per loop!

## Slide 74: Software Pipelining and Trace Scheduling
Iteration 0
Iteration 1
Iteration 2
Iteration 3
Iteration 4

## Slide 75: Example of Software Pipelining
Loop: LDR R0, [R1]
ADD R4, R0 R2
STR R4, [R1]
SUB R1, R1, #4
BNE R1, Loop
Iteration i: LDR R0, [R1]
ADD R4, R0, R2
STR R4, [R1]
Iteration i + 1: LDR R0, [R1]
ADD R4, R0, R2
STR R4, [R1]
Iteration i + 2: LDR R0, [R1]
ADD R4, R0, R2
STR R4, [R1]

## Slide 76: Speculation….
What is Speculation
  Idea is to overcome control dependence by speculating on the outcome of the branches and executing the program as if our guesses were correct
Speculation is going one step ahead of “Dynamic Speculation with branch prediction” where the guessed instructions are only fetched and issued but not executed
Instruction execution with speculation is a four step process;
  Issue
  Execute
  Write Result in the Reorder Buffer (ROB)
  Commit
How much should one speculate? Over multiple branches?

## Slide 77: Trace Scheduling
Parallelism across IF branches vs. LOOP branches
Two steps:
  Trace Selection
  Find likely sequence of basic blocks (trace)
  of (statically predicted or profile predicted)
  long sequence of straight-line code
– Trace Compaction
  Squeeze trace into few VLIW instructions
  Need bookkeeping code in case prediction is wrong
Compiler undo bad guess (discards values in registers)
Subtle compiler bugs mean wrong answer vs. poorer performance; no hardware interlocks

## Slide 78: How much to speculate?
Speculation Pro: uncover events that would otherwise
stall the pipeline (cache misses)
Speculation Con: speculate costly if exceptional event
occurs when speculation was incorrect
Typical solution: speculation allows only low-cost
exceptional events (1st-level cache miss)
When expensive exceptional event occurs, (2nd-level cache miss or TLB miss) processor waits until the instruction causing event is no longer speculative before handling the event
Assuming single branch per cycle: future may speculate across multiple branches!

## Slide 79: Architecture Comparison
 | Cortex A9 | Cortex A15 | Qualcomm Scorpion | Qualcomm Krait
Decode Width | 2 wide | - | 2 wide | 3 wide
Pipeline Depth | 8 | 14 | 10 | 11
Issue Width | 2 | 8 (?) | 3 | 4
OoO execution | Y | Y | Partial | Y
FPU | Optional VFPv3-D16 Pipelined | VFPv3 Pipelined | VFPv3 Pipelined | VFPv3 Pipelined
NEON | Optional MPE, 64 bit | Y | Y 128 bit | Y 128 bit
Process Technology | 40 | 32/28 | 40 | 28
Clock Speed | 1-1.2 GHz | 1.5 – 2.5 GHz | 1.2GHz | 1.5GHz

## Slide 80: Next session…
Limits on ILP…
What is the alternative to decrease CPI?
Software holds the key to future performance enhancement…